## Slide 1
Integrated Daylight Simulation

## Slide 2
Tas daylight is based on adaptive radiosity
CIE 171,2006 compliant
Daylight Render

## Slide 3
Fast multi-zone daylight simulations
Multi-core processing

## Slide 4
Direct & diffuse daylight simulation and solar shading
Inside & outside specular reflection analysis Uses ray tracing over radiosity results

## Slide 5
Tas Climate Based Daylight Modelling
Climate based daylight modelling originated in the lighting simulation community. Hourly diffuse and direct solar radiation climate data is used to produce daylight coefficients for patches of sky. Irradiance data is converted to illuminance using a luminous efficacy model. The daylight contribution to the space is then calculated hourly through the year for each sky patch.
EDSL’s Tas software has originated in the thermal simulation community. Our Tas software calculates the diffuse and direct solar distribution in spaces hourly through the year. We have developed a daylighting simulation engine, which is fully integrated with our thermal simulation engine. We are, therefore, able to calibrate the daylight contribution from the solar contribution in a space using luminous efficacy. Put simply, we convert the hourly solar income into hourly daylight income.
The following slides illustrate the functionality of the combined thermal and daylight simulation model on a classroom.

## Slide 6
Climate Based Daylight Modeling
Calibrate sampled beam & diffuse daylight analysis against equivalent solar gains from thermal simulations.
Calculate daylight levels from hourly solar gain over a year to produce UDI, DA, daylight distribution

## Slide 7
Tas allows specific spaces from a large model to be selected for individual analysis.
A complete range of analysis may be undertaken on the selected space(s) without having to simulate the entire building model.
Here a classroom has been selected to produce CBDM metrics and adaptive comfort analysis.
The roof has been made transparent in the display to show internal layout.

## Slide 8
15.00 hours, end of March:
Direct sunlight patches visible through the windows

## Slide 9
Plan View of Classroom:
Clear sky daylight simulation shows daylight lux level distribution
15.00 hours, end of March:

## Slide 10
False colour daylight distribution for the same hour
15.00 hours, end of March:

## Slide 11
This new configuration of the south wall’s windows has the middle row removed.
The high level windows still throw light to the back of the space.
The view is maintained by the lower row of windows.

## Slide 12
Daylight analysis: 15:00 hours, end of March
A useful amount of daylight is reaching the back of the room via the high level windows.
The amount of direct sunlight next to the windows is reduced.

## Slide 13
Daylight analysis: 15:00 hours, end of March
Original Configuration
Revised Configuration
Daylight analysis: 15:00 hours, end of March
Original: 3 rows of windows at south wall
Revised: 2 rows, middle row removed

## Slide 14
This time the UDIa (UDI - acceptable) is at 85% giving a very good performance.
UDIe (UDI Exceedance) is at an acceptable level.
High level windows have given a good general distribution of daylight
Low level view windows do not produce excessive glare.

## Slide 15
An alternative to removing the middle row of windows would be to provide some solar shading to reduce the direct sunlight
through these windows.
This façade solution is
but one of
many that
would comply with the
CBDM
criteria
This configuration also had
good CBDM metrics.
Both configurations
worked well on all
orientations.

## Slide 17
Classroom analysis shading configuration optimised for:
shade blade width
vertical spacing
angle
CBDM

## Slide 18
Shadowcast Studies
Context Analysis
Daylight Views

## Slide 19
Tas Natural Ventilation Studies
Tas Engineering also offers integrated Natural Ventilation and solar gain (insolation) analysis.
Please visit our website for more details