Part L2 for Warehouse

Constructions

Ground Floor U-value = 0.07W/m²K

External wall:

Two types:

Brick, cavity, insulation, block U = 0.30W/m2K

Lightweight aluminium clad wall U = 0.35W/m²K

Roof: Metal with insulation U =0.25W/m²K

Internal floors made up from cavity, concrete and carpet

Rooflights: Clear low-e glass: U = 1.93W/m²K (see below)

Glazing: Saint Gobain SKN165, U=1.63W/m2K (see below)

All frames were aluminium.

Other Information

The warehouse was mechanically ventilated, with VRFs in some areas. The supply and extract fans had a total SFP of 2.28 W/l/s

Most areas were supplied with 11.24m3/s of fresh air heated to 16°C with 60% heat recovery.

The warehouse areas were heated by gas fired heaters with an efficiency of 91.1%. Most of the offices were heated by the gas boiler with a 90% efficiency. Some areas had VRFs with a COP of 4.2 for both heating and cooling.

The VRFs had an SFP of 0.8 at 8 air changes per hour.

Domestic hot water was provided by the 90% efficient gas boiler.

The building had automatic monitoring and targeting with alarms for out of range values, and a power factor correction of 0.95

Results

As this chart shows, the Design building’s CO2 emissions were much lower than the target emission rate (TER), so the building passed this part of Part L2 with ease.